## Slide 1
Application
Security
Frame
Packet
Protection
UDP
Application
Security
Frame
Packet
Protection
UDP
Client
Server

## Slide 2
Application
Security
Frame
Packet
Protection
UDP
Mirror
Shim
UDP
TLS 1.3
Net
Server
Client

## Slide 3
Client
Server
Client
Server
Client
Server
TCP
TCP + TLS1.2
QUIC 0RTT + TLS1.3
TCP Handshake
Data
TLS 1.2 Handshake

## Slide 4
Client
Server
TCP Handshake
Data
TLS 1.2 Handshake
SN1
SN2
SN3
SN4
SN5
SN2
SN1
SN3
SN4
SN5

## Slide 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | T | T | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Version (32) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DCID Len (8) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination Connection ID (0…160) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCID Len (8) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Source Connection ID (0…160) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Type | Name
0x0 (00) | Initial
0x1 (01) | 0-RTT
0x2 (10) | Handshake
0x3 (11) | Retry

## Slide 6
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | S | R | R | K | P | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination Connection ID (0…160) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Packet Number (8/16/24/32) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Protected Payload (*) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stream ID (i) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
[Offset (i)] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
[Length (i)] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Stream data(*) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | T | T | E | E | E | E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Version (32) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | S | E | E | E | E | E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination Connection ID (0…160) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Packet Number (8/16/24/32) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Skipped part (0/8/16/24) |  |  |  |  |  |  | 
Sample Protected Payload (128) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Protected Payload (*) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Long Header
Short Header
Common fields

## Slide 9
Ivy Mirror
TLS
Network
Tested
Implementation

## Slide 10: 2.Streams

## Slide 11
Stream types and
Identifier
Stream
Unidirectional
Bidirectional
Identified by Stream ID of 2^62-1
LSB of Stream ID

## Slide 12
Sending and
Receiving Data
Application
STREAM Frames sent
Data produce
Ordered Byte Stream recv
Ensure flow control
Buffer any out of order data
Duplicate discard
PROTOCOL_VIOLATION
Same offset BUT
Different data
Same offset BUT
Different data

## Slide 13
Stream Prioritization
Stream multiplexing
Resources allocated correctly prioritized
Application
Information on priority

## Slide 14
Operations on Streams
Application
STREAM+FIN
Sending
Receiving
Write data
Clean Terminaison
Abrupt Terminaison (Reset)
Read data
Abort reading + request closure
RESET_STREAM
STOP_SENDING

## Slide 15: 3.Streams state

## Slide 16
Ready
Send
Data Sent
Reset Sent
Reset Recvd
Data Recvd
s.RESET_STREAM
s.RESET_STREAM
s.RESET_STREAM
r.ACK
rAll.ACK
s.STREAM + FIN
s.STREAM
s.STREAM_DATA_BLOCKED
Peer Create Bidirectional Stream
Create Stream (Sending)
Peer Create Bidirectional Stream
sending
receiving
Terminal state
Sending Stream States

## Slide 17
Recv
Size Known
Data Recvd
Reset Recvd
Reset Read
Data Read
r.RESET_STREAM
r.RESET_STREAM
[r.RESET_STREAM]
app.read.RST
rAll.data
app.read.all data
r.STREAM + FIN
r.STREAM / r.RESET_STREAM/ r.STRAM_DATA_BLOCKED
Create Bidirectional Stream (Sending)
r.MAX_STREAM_DATA / r.STOP_SENDING (Bidirectional)
Create Higher-Numbered Stream
[r.ALL data]
Receiving Stream States
Notes: 3,3 check

## Slide 18
Bidirectional Stream States
idle
Open
Half-Closed
(remote)
Half-Closed
(local)
Closed
Ready
Recv
Send
Reset Sent
Data Sent
Reset Recvd
Data Recvd
Size Known
Reset Recvd
Data Recvd
Reset Read
Data Read
Notes: 3,3 check

## Slide 19: 4.Flow Control
Notes: It is necessary to limit the amount of data that a receiver could
buffer, to prevent a fast sender from overwhelming a slow receiver,
or to prevent a malicious sender from consuming a large amount of
memory at a receiver. To enable a receiver to limit memory
commitment to a connection and to apply back pressure on the sender,
streams are flow controlled both individually and as an aggregate. A
QUIC receiver controls the maximum amount of data the sender can send
on a stream at any time
/!\ Data sent in CRYPTO frames is not flow controlled in the same way as stream data.

## Slide 20
Data Flow Control
Advertise sender of limits
Stream Control Flow
Receiver
Connection Control Flow
limiting the amount of data that can be sent on any stream
limiting the
total bytes of stream data sent in STREAM frames on all streams.
MAX_STREAM_DATA
MAX_DATA
FLOW_CONTROL_ERROR
Sender
A sender MUST ignore any MAX_STREAM_DATA or MAX_DATA frames that do not increase flow control limits.
ELSE
Increase Limit
Advertise receiver of limits reach
STREAM_DATA_BLOCKED || DATA_BLOCKED
Connection close
If idl
Notes: A sender MUST ignore any MAX_STREAM_DATA or MAX_DATA frames that do not increase flow control limits.
Flow Control Performance: If an endpoint cannot ensure that its peer always has available flow control credit that is greater than the peer's bandwidth-delay product on this connection, its receive throughput will be limited by flow control. Packet loss can cause gaps in the receive buffer, preventing the application from consuming data and freeing up receive buffer space. Sending timely updates of flow control limits can improve performance. Sending packets only to provide flow control updates can increase network load and adversely affect performance. Sending flow control updates along with other frames, such as ACK frames, reduces the cost of those updates.

## Slide 21
Handling Stream Cancellation
Endpoint
Ignore further data arriving on that stream
RESET_STREAM

## Slide 22
Stream Final Size
Final Size
N° of byte sent on one stream
field in
STREAM+FIN Frame
FINAL_SIZE_ERROR
If a RESET_STREAM or STREAM frame is received indicating a change in the final size for the stream

## Slide 23
Controlling Concurrency
Endpoint
limits the cumulative number of incoming streams a peer
can open
TRANSPORT_PARAMETER_ERROR
(StreamID < max_stream*4 + initial_stream_id_for_type
OR
StreamID < MAX_STREAMS*4 + initial_stream_id_for_type)
AND
IGNORE MAX_STREAMS advertising smaller limit
MAX_STREAMS > 2^60
FRAME_ENCODING_ERROR
max_stream > 2^60
STREAM_LIMIT_ERROR
SteamID exceed
Unable to open new Stream
STREAMS_BLOCKED

## Slide 24: 5.Connection
Notes: QUIC's connection establishment combines version negotiation with the cryptographic and transport handshakes to reduce connection establishment latency, as described in Section 7. Once established, a connection may migrate to a different IP or port at either endpoint as described in Section 9. Finally, a connection may be terminated by either endpoint, as described in Section 10.

## Slide 25
Connection ID
Endpoint
Set of connection IDs
selects connection IDs using an implementation-specific
In NEW_CONNECTION_ID frame
Packet with long header
Packet with short header
Source Connection ID
Destination Connection ID
Omit explicit length of CID
Destination Connection ID
Echo the CIDs selected by client
Version Negociation Packet
0 length CID
No need to route to correct endpoint
Notes: Connection IDs MUST NOT contain any information that can be used by an external observer.
A zero-length connection ID can be used when a connection ID is not needed to route to the correct endpoint. However, multiplexing connections on the same local IP address and port while using zero- length connection IDs will cause failures in the presence of peer connection migration, NAT rebinding, and client port reuse; and therefore MUST NOT be done unless an endpoint is certain that those protocol features are not in use.
When an endpoint uses a non-zero-length connection ID, it needs to ensure that the peer has a supply of connection IDs from which to choose for packets sent to the endpoint. These connection IDs are supplied by the endpoint using the NEW_CONNECTION_ID frame (Section 19.15).

## Slide 26
Issuing/Consuming and Retiring CIDs
Endpoint
Seqnum = 0|1
Random Source Connection ID in long header of Initial packet
active_connection_id_limit parameter to advertise le n° of active cid
Initial CID
Additional CID
NEW_CONNECTION_ID
Seqnum ++
Seqnum not assigned*
From Retry Packet
Issued CID Invalidate
RETIRE_CONNECTION_ID
Consummed CID
Migrating peer
RETIRE_CONNECTION_ID
NEW_CONNECTION_ID
increased Retire Prior To field
[RETIRE_CONNECTION_ID]
Connection close
can no longer process the indicated CIDs,
CONNECTION_ID_LIMIT_ERROR
active_connection_id_limit
reach
Notes: Each Connection ID has an associated sequence number to assist in detecting when NEW_CONNECTION_ID or RETIRE_CONNECTION_ID frames refer to the same value. The initial connection ID issued by an endpoint is sent in the Source Connection ID field of the long packet header (Section 17.2) during the handshake. The sequence number of the initial connection ID is 0. If the preferred_address transport parameter is sent, the sequence number of the supplied connection ID is 1.
A NEW_CONNECTION_ID frame might cause an endpoint to add some active connection IDs and retire others based on the value of the Retire Prior To field. After processing a NEW_CONNECTION_ID frame and adding and retiring active connection IDs, if the number of active connection IDs exceeds the value advertised in its active_connection_id_limit transport parameter, an endpoint MUST close the connection with an error of type CONNECTION_ID_LIMIT_ERROR.
An endpoint might need to stop accepting previously issued connection IDs in certain circumstances. Such an endpoint can cause its peer to retire connection IDs by sending a NEW_CONNECTION_ID frame with an increased Retire Prior To field. The endpoint SHOULD continue to accept the previously issued connection IDs until they are retired by the peer. If the endpoint can no longer process the indicated connection IDs, it MAY close the connection.

## Slide 27
Matching Packets to Connections
Incoming packet
Existing connection
No existing connection
length Destination Connection ID != 0
Destination CID corresponding
Existing connection with 0-length
length Destination CID ==0
Destination CID corresponding
(only port and address)
Create new Connection
Connection Unusable
If packets inconsistent with
state of connection
(wrong version, protection, …)
Packet discards
Stateless Reset
Notes: If the Destination Connection ID is zero length and the addressing
information in the packet matches the addressing information the
endpoint uses to identify a connection with a zero-length connection
ID, QUIC processes the packet as part of that connection. An
endpoint can use just destination IP and port or both source and
destination addresses for identification, though this makes
connections fragile as described in Section 5.1.

## Slide 28
Client Packet Handling
Client Receive Packet
DestinationCID 0-length
no
Packet discard
DestinationCID matches client choosen value
Client accept 0-length ID
no
no
yes
Match port and local address to identify connection
yes
no
Encryption Key
Computed
yes
Packet buffered
no
Version corresponding
yes
no
Notes: Due to packet reordering or loss, a client might receive packets for
a connection that are encrypted with a key it has not yet computed.
The client MAY drop these packets, or MAY buffer them in anticipation
of later packets that allow it to compute the key.

## Slide 29
Server Packet Handling
Server Receive Packet
Supported Version
no
Packet discard
Large enough to init any supported version
[Limit of negotiation reach]
yes
no
Send Version Negotiation
no
Match with CID or port/address
yes
Match with CID or port/address
no
Start handshake
Packet =
Initial
Refuse connection Initial(Connection_close)
[Packet buffered]
Packet =
0-RTT
else

## Slide 30
Considerations for Simple Load Balancers
Final Size
N° of byte sent on one stream
field in
STREAM+FIN Frame
FINAL_SIZE_ERROR
If a RESET_STREAM or STREAM frame is received indicating a change in the final size for the stream

## Slide 31
Life of a QUIC Connection
Final Size
N° of byte sent on one stream
field in
STREAM+FIN Frame
FINAL_SIZE_ERROR
If a RESET_STREAM or STREAM frame is received indicating a change in the final size for the stream

## Slide 32
Operations on Connections
Application
Server Role
yes
Client Role
Open Connection
Enable Early Data when available
Informed Early Data when accepted/rejected
Listen for incomming connection
Early Data available
Embed app-control data in TLS ticket sent to client
Retrieve app-control data from client’ticket and accept OR
Reject
no
configure minimum values for the initial number of permitted streams of each type
control resource allocation for receive buffers by setting flow
control limits both for streams and for the connection
Identify handshake completion
Keep connection alive
Close connection

## Slide 33: 6.Version Negotiation

## Slide 34
Sending Version Negotiation Packets
New Connection on server and version selected by client not supported
Client receive list of version
Version Negociation packet
-> 1st UDP datagram need enough size
« Error »
Version Negociation packet

## Slide 35
Handling Version Negotiation Packets
Client receive Version Negociation
Already process any other packet
List version already selected by the client
Packet discard
Connection closed
Only supported selected version
? To be defined in the futur

## Slide 36
Using Reserved Versions
Final Size
N° of byte sent on one stream
field in
STREAM+FIN Frame
FINAL_SIZE_ERROR
If a RESET_STREAM or STREAM frame is received indicating a change in the final size for the stream

## Slide 37: 7. Cryptographic and Transport Handshake

## Slide 38: 10.Connection Termination

## Slide 39
Immediate close
Closing connection
Draining connection
r.CONNECTION_CLOSE
Connection close sent
s.CONNECTION_CLOSE
Signal rcv
[r.CONNECTION_CLOSE
|| r.stateless_RESET]
Connection close
Connection close (faster)
Closing/draining
period finish
If no new socket open
(no new response allow -> close asap)
All stream closed
Notes: 10,1
?? Once the closing or draining period has ended, an endpoint SHOULD discard all connection state.
This results in new packets on the connection being handled generically.
For instance, an endpoint MAY send a stateless reset in response to any further incoming packets.

## Slide 40
Idle timeout
idle
max_idle_timeout (=min(max_peer1,max_peer2))
specified and exceed both peers
+ > 3 * ProbeTimeOut
Closing connection
Draining connection
Connection close sent
s.CONNECTION_CLOSE
Signal rcv
[r.CONNECTION_CLOSE
|| r.stateless_RESET]
Connection close
Connection close (faster)
Closing/draining
period finish
If no new socket open
(no new response allow -> close asap)
Notes: 10,2
https://tools.ietf.org/html/draft-ietf-quic-recovery-29
LIVENESS
An endpoint that sends packets close to the effective timeout risks having them be discarded at the peer, since the peer might enter its draining state before these packets arrive
An endpoint can send a PING or another ack-eliciting frame to test the connection for liveness if the peer could time out soon, such as within a PTO; see Section 6.2 of [QUIC-RECOVERY].
This is especially useful if any available application data cannot be safely retried. Note that the application determines what data is safe to retry.

## Slide 41
Stateless reset
Closing connection
Draining connection
If StatelessResetToken field = 1
And r.CONNECTION_CLOSE
And r.RETIRE_CONNECTION_ID
And Unpredictable Bits field > 38 bits
Connection close sent
s.CONNECTION_CLOSE
Signal rcv with
Connection_close
[r.CONNECTION_CLOSE
|| r.stateless_RESET]
Connection close
Connection close (faster)
Closing/draining
period finish
If no new socket open
(no new response allow -> close asap)
All stream closed
Cancel
TOREAD
Notes: A minimum size of 21 bytes does not guarantee that a stateless reset
is difficult to distinguish from other packets if the recipient
requires the use of a connection ID. To prevent a resulting
stateless reset from being trivially distinguishable from a valid
packet, all packets sent by an endpoint SHOULD be padded to at least
22 bytes longer than the minimum connection ID that the endpoint
might use. An endpoint that sends a stateless reset in response to a
packet that is 43 bytes or less in length SHOULD send a stateless
reset that is one byte shorter than the packet it responds to.
These values assume that the Stateless Reset Token is the same length
as the minimum expansion of the packet protection AEAD. Additional
unpredictable bytes are necessary if the endpoint could have
negotiated a packet protection scheme with a larger minimum
expansion.

## Slide 42: 11.Error Handling

## Slide 43
Connection Errors
Error detected
Obvious violation entire connection
| corruption of state
Error Signaled
s.CONNECTION_CLOSE
Connection close
[May close]

## Slide 44
Stream Errors
Error detected
Obvious violation 1 stream
| corruption of state
Error Signaled
s.RESET_STREAM |
s.STOP_SENDING
Stream close
[May close]

## Slide 45: 12.Packet and Frames

## Slide 46
Protected packet
Initial packets
(all exept Version Negotiation)
All other packet
Keys staticallly derived
Keys derived from crypto handshake

## Slide 47
Coalescing packet
Coalesce multiple QUIC packet in one UDP datagram
Length field of Initial/0-RTT/Handshake/1-RTT packets
if receiver able for a single connection (same connection id)

## Slide 48
Packet number
Packet number
0-2^62-1
Determine the cryptographic nonce for packet protection
(enforce crypto separation)
Packet number in short or long header
Encoded in 1 to 4 bytes
Initial space
Handshake space
Application data space
Initial packets
Handshake packets
0-RTT and 1-RTT packets
Connection close
N° sending reach 2^62-1
(without connection_close)
Notes: Determined by the Largest Acknoledged field of Ack

## Slide 49
Frames
Contain at least 1 frame
If not Version Negociation | Stateless Reset | Retry packets
I: Initial (Section 17.2.2)
H: Handshake (Section 17.2.4)
0: 0-RTT (Section 17.2.3)
1: 1-RTT (Section 17.3)
ih: A CONNECTION_CLOSE frame of type 0x1d cannot appear in Initial or Handshake packet